Specification of 500/800 rewinding machine

1. Main parameter:

| 1.1 | Model No.: | 500/800mm |
| --- | --- | --- |
| 1.2 | Suitable material | Copper wire、Aluminum wire、Insulation wire |
| 1.3 | Max diameter of wire | Copper wire: 3.0mm Aluminum wire: 4.0mm Insulation cable : 1.0-6.0mm² |
| 1.4 | Suitable bobbin size | 500/800mm |
| 1.5 | Max loading | 600kg |
| 1.6 | Rewinding speed | 0-250 m/min |

2. The main components:

| 2.1 | 500/800mm pay off with motor driving | 1 set |
| --- | --- | --- |
| 2.2 | Wire guider | 1 set |
| 2.5 | 500/800mm take up and transverse | 1 set |

3. Detailed technical description:

3.1 500/800mm pay off with motor driving

| 3.1.1 | Bobbin size | 500-800mm |
| --- | --- | --- |
| 3.1.2 | Max speed | 250 m/min |
| 3.1.3 | Speed control | Automatically control by dancer |
| 3.1.4 | Loading/unloading | Manual hydraulic |
| 3.1.5 | Clamping/releasing | Pneumatic |
| 3.1.6 | Motor | 4KW AC motor |
| 3.1.7 | Motor control | Inventor control |
| 3.1.8 | Brake | Pneumatic brake |
| Detail Specification |
| Motorize cable-sending unit is available, machine completed with bobbin driven system. |
| Application: for cable pay off in the process of cable manufacturing or rewinding. |
| Shaft-less type, open and close of arms is done by handle screws manually. |
| A slip type torque limit to be fitted on each driven unit to getting a just locking tension on the bobbin. |
| Safety control: |
| Bobbin lifting up and down limit positions control protection. |
| Bobbin close and open limit positions control protection. |

3.2. 500/800mm take up and transverse

| 3.2.1 | Bobbin size | 500-800mm |
| --- | --- | --- |
| 3.2.2 | Max speed | 250m/min |
| 3.2.3 | Loading/unloading | Manual hydraulic |
| 3.2.4 | Clamping/releasing | Pneumatic |
| 3.2.5 | Motor | 4KW AC motor |
| 3.2.6 | Motor control | Inventor control |
| 3.2.7 | Traverse | Polished rod traversing |
| 3.2.8 | Meter counter | Digital type |
| Detail Specification |
| Application: for cable pay off in the process of cable manufacturing or rewinding. |
| A slip type torque limit to be fitted on each driven unit to getting a just locking tension on the bobbin. |
| Safety control: |
| Bobbin lifting up and down limit positions control protection. |
| Bobbin close and open limit positions control protection. |

4. Electrical control system

| 4.1 | Main low-voltage components : Schneider brand |
| --- | --- |
| 4.2 | Main motor AC motor: SIEMENS brand |
| 4.3 | AC driver system: SIEMENS brand |
| 4.4. | Touch panel: SIEMENS brand |
| 4.5. | PLC: SIEMENS brand |

5. Drawing

| 5.1 | Machine layout, foundation drawing |
| --- | --- |
| 5.2 | Electricity, piping drawings |
| 5.3 | Operation manual |
| 5.4 | The principle drawing of the electrical system |
| 5.5 | The list of the cable. |

6. Other

| 6.1 | The operation direction of the machine: right hand or based on the customer’s requires. |
| --- | --- |
| 6.2 | Machine color: according to the color plate offered by customers. |
| 6.3 | The bobbin: according to the drawing offered by customers. |

SHANGHAI SHINEWORLD ENGINEERING CO., LTD.

2020.12.29